## Slide 1: Introduction to Modern Sequencing Technologies
Kirsten McLay
Platform and Pipelines Operations Manager

## Slide 2
Overview
History of DNA Sequencing
Introduction
NGS Technology Platforms
New Technologies
Platform
Summary

## Slide 3
Timeline
James Watson and Francis Crick,1953

## Slide 4
Timeline
Between 1975-1977 three methods of DNA sequencing were published
Sanger - Coulson Plus-Minus method
Maxam - Gilbert method
Fred Sanger’s chain termination method

## Slide 5
Timeline
1953 Discovery of the structure of the DNA double helix.
1972 Development of recombinant DNA technology, which permits isolation of defined fragments of DNA
1975 The first complete DNA genome to be sequenced is that of bacteriophage φX174
1977 Allan Maxam and Walter Gilbert publish "DNA sequencing by chemical degradation".
  Frederick Sanger independently publishes "DNA sequencing by enzymatic synthesis".
1980 Frederick Sanger and Walter Gilbert receive the Nobel Prize in Chemistry
1984 Medical Research Council scientists decipher the complete DNA sequence of the Epstein-Barr virus, 170 kb.
1986 The first semi-automated DNA sequencing machine developed
1987 Applied Biosystems markets first automated sequencing machine, the model ABI 370.
1990 large-scale sequencing trials on Mycoplasma capricolum, Escherichia coli, Caenorhabditis elegans, and Saccharomyces cerevisiae
1990 The Human Genome Project is officially launched
1995 the first complete genome of a free-living organism, the bacterium Haemophilus influenzae is published. The circular chromosome contains 1,830,137 bases
1995 Fluorescence energy transfer dye-based sequencing technology is published.
2003 Completion of The Human Genome Project

## Slide 6
Sanger Sequencing Technology

## Slide 7: Sanger dideoxy sequencing
GAAGCTGCGTCAACACGCGTGCAAACGC
CTTCGACGCAGTTGTGCGCACGTTTGCG
Denature – heat to 96°C

## Slide 8: Sanger dideoxy sequencing
CTTCGACGCAGTTGTGCGCACGTTTGCG
GAAGCTGCGTCAACACGCGTGCAAACGC
CTTCGACGCAGTTGTGCGCACGTTTGCG
GAAGCTGCGTCAACACGCGTGCAAACGC
-T-
-C-
-A-
-G-
-T-
-C-
-A-
-G-
-T-
-C-
-A-
-G-
-T-
-C-
-A-
-G-

## Slide 9: Sanger dideoxy sequencing
CTTCGACGCAGTTGTGCGCACGTTTGCG
GAAGCT
-T-
-C-
-A-
-G-
-T-
-C-
-A-
-G-
-T-
-C-
-A-
-G-
-T
-C-
-A-
-G-
AAGCT
TTCGA
Cool to 50oC
Heat to 60oC

## Slide 10: Sanger dideoxy sequencing
GAAGCT
AAGCT
TTCGA
CTTCGACGCAGTTGTGCGCACGTTTGCG
-T-
-C-
-A-
-G-
-T-
-C-
-A-
-G-
-T-
-C-
-A-
-G-
-T
-C-
-A-
-G-
-T
-T
GAAGCTGCGT
CTTCGACGCAGTTGTGCGCACGTTTGCG
AAGCT
TTCGA
GAAGCTGCGTCAACACGCGT
CTTCGACGCAGTTGTGCGCACGTTTGCG
AAGCT
TTCGA

## Slide 11: Sanger dideoxy sequencing
CTTCGACGCAGTTGTGCGCACGTTTGCG
GAAGCTGCGTCAACACGCGTG
GAAGCTGCGTCAACACGCGT
GAAGCTGCGTCAACACGCG
GAAGCTGCGTCAACACGC
GAAGCTGCGTCAACACG
GAAGCTGCGTCAACAC
GAAGCTGCGTCAACA
template
G
GA
GAAGCTGCGTCAAC
GAA
GAAGCTGCGT
GAAGCTGCG
GAAGCTGC
GAAGCTG
GAAGCT
GAAGC
GAAG
GAAGCTGCGTCAA
GAAGCTGCGTCA
GAAGCTGCGTC
GAAGCTGCGTCAACACGCGTGCAAACGC
result
Over 45 cycles of 95o, 50o and 60o

## Slide 12: Sanger dideoxy sequencing
-
+
A
A
G
C
T
laser
G

## Slide 13
Sequence output

## Slide 16
BRACA2

## Slide 17
Exon Resequencing

## Slide 18
Notes: 1) Antarctic diatom 2) Influenza 3) Moss (Physcomitrella patens) 4) White campion 5) Red clover 6) Tomato 7) Pea 8) Listeria 9) 10) Chloroplasts 11) Broad bean 12) Rapeseed 13) Barley 14) Willow15) Barrel clover 16) Tongue metagenome 17) FIV 18) Arabidopsis 19) Oats 20) Fungus21) Fission yeast 22) Mouse 23) Naked Mole Rat 24) Wheat 25) Perennial grass 26) Glomus intraradices 27) Immortal jellyfish 28) Cow 29) Kentish Plover 30) Common cuttelfish 31) Liver fluke 32) Green peach aphid 33) Late instar larvae 34) Dog 35) Turkey 36) Chicken 37) Amphioxus 38) Drosophila 39) Passionflower butterfly 40) Carp 41) White fly

## Slide 19
Chart: 
| Rice | Maize | Human | Barley | Wheat
Size of various Genomes in Megabases | 0.4 | 2 | 3 | 5 | 17
Size of various genomes in Gb

## Slide 20
NGS
Improvements in Sequence Data Generation
$10
$1.0
$0.1
$0.01
$0.001
Cost / kb

## Slide 22
Modern Sequencing Technologies
High-throughtput sequencing platforms
  Roche 454
  Ion Torrent
  Illumina MiSeq & HiSeq
  PacBio RSII & Sequel
  Oxford Nanopore MinION & PromethION
Optical mapping platforms

## Slide 23
Roche 454

## Slide 24
Sample Input and Preparation
Library Preparation
One fragment = One bead
emulsionPCR amplification
One bead = one read
Data Analysis
~29µm

## Slide 25
Roche 454

## Slide 26
Advantages
Longer read length (up to 400bp-800bp)
Faster run (~10 hours)
Limitations
Clonal amplification of sample on beads – requires 1 DNA fragment / bead or signal mixed
Homopolymers – limited resolution of poly N signals
Applications
Bacterial genomes
Expressed gene sequences (mRNA)
Targetted gene sequencing (amplicons)

## Slide 27
Ion Torrent

## Slide 28
Thermo (Life Technologies)
Currently available
  Ion PGM
    Bench-top
    1-2Gb output in 4-8hrs
    Up to 400bp reads
  Ion Proton
    Bench-top
    10Gb output in 4 hours
    200bp reads

## Slide 29
Technology
Semiconductor sequencing
Detects the release of hydrogen ions on that are released on polymerisation of DNA – a non-optical method (pH change)
A microwell is flooded with a single nucleotide. If this is complementary to the leading template nucleotide in the well (bound to a bead) it is incorporated, and this is detected by the semiconductor.

## Slide 30
Sequencing Chemistry

## Slide 31
Semiconductor Sequencing

## Slide 32
Run Summary

## Slide 33
Advantages
  Fast run time
  Machine costs are low
Limitations
  Can’t resolve homopolymers
  Single nucleotide cycles
  Cumbersome library prep
    Emulsion PCR step
Applications
  High throughput amplicon
  Bacterial genomes
  Metagenomes
  Transcriptomics

## Slide 34
Illumina

## Slide 35
Currently available
  Illumina MiSeq
    Bench-top
    Up to 15Gb output in 2 days
    Up to 300b reads
  Illumina NextSeq
    Bench-top
    Up to 120Gb in 30 hours
    Up to 150b reads
  Illumina HiSeq
    Very high throughput
    2500, 3000, 4000 and X models
    Up to 1.8Tb in 3.5 days
    Up to 250b reads (2500 only)

## Slide 36
Sequencing-by-synthesis, with reversible dye terminators
Detects the release of fluorescence of nucleotide incorporation from clusters of identical fragments bound to a glass flowcell
At the end of a ‘cycle’ excess terminators and the ‘blocker’ which prevents incorporation of more than one nucleotide are washed away

## Slide 37
Advantages
  A machine for all budgets
  Very accurate sequencing
  Single cycle reads all nucleotides
Limitations
  Read length shorter than others
Applications
  Amplicon resequencing
  Targeted sequencing
  Bacterial genomes
  Metagenomics
  Transcriptomics
  Large genomes

## Slide 38
Technology Platforms - Illumina
HiSeq2000 x 1
HiSeq2500 x 4
HiSeq4000 x 2
MiSeq x 3
Illumina Platforms at EI

## Slide 39
cBot Clustering

## Slide 40
‘Lawn’ of short adapter DNA strands
Illumina Flowcell Overview

## Slide 41
Hybridise and extend

## Slide 42
Bridge Amplification

## Slide 43
Final step on cBOT is to hybridise the sequencing primer
What is sequenced?

## Slide 44
Uses Time Delay Integration – continuous scanning
Illumina HiSeq

## Slide 45
Two overlapping clusters may have the same cycle 1 base
Cluster detection is calculated in cycles 1- 4
Cluster detection
Aim for ~ 850,000 clusters/mm² and balanced
representation of each of the four bases at the
beginning of each read
Notes: Challenges faced with RAD_seq projects – low diversity samples eg 16S, Amplicon
Discuss – staggered barcoding, lowering cluster density, elevating PhiX control

## Slide 46
Incorporate 1 fluorescent nucleotide
Excite and image fluorescence
Cleave terminator and fluorophore
Repeat process
SBS Sequencing Chemistry

## Slide 47
SBS Sequencing Chemistry
Basecalling : The identity of each base of a cluster is identified from sequential images

## Slide 48
SBS Sequencing Chemistry
HiSeq 2500, NextSeq and MiSeq
- clusters formed randomly on the surface of the flowcell
HiSeq 3000, 4000
- clusters only form within nanowells
- patterned flowcells
NextSeq
utilises 2-colour instead of 4-colour chemistry resulting in faster sequencing time
T- green A - both
C – red G – no dye

## Slide 49
Illumina
Notes: As multiplexing has increased – high throughput automation – liquid handling platforms
Perkin Elmer, Beckman Coulter, Hamilton

## Slide 50
Pacific Biosciences

## Slide 51
Technology Platforms - PacBio
PacBio RSII
Waste
Blade Centre
SMRT cells/Tips
Reagents/Samples
RS Touch

## Slide 52
PacBio RSII
  PacBio RSII
    Definitely not benchtop!
    Read lengths up to 60kb
    6 hour run time
    1Gb output
    Single molecule resolution
      SMRT = single molecule real-time
    Direct methylation detection

## Slide 53
Technology
Sequencing by synthesis
No terminator chemistry
SMRT cells contain 150,000 ZMWs (well)
ZMW (zero-mode waveguide) wells have a single DNA polymerase bound Single stranded DNA is fed into the wells along with fluorescently labelled nucleotides
Wells are smaller than the wavelength of the light is beamed in, giving very precise illumination of the polymerase alone
Emission is measured for basecalling

## Slide 54
PacBio Sequencing Technology
Signal Processing and Basecalling – conversion of pulses of light into DNA bases and kinetic measures

## Slide 55
PacBio RSII
Advantages:
  No amplification of DNA required
  Rapid sequencing – up to 1 Gb in 360 mins
  Long reads – currently 20kb with plans to extend
  Potential for sequencing modified nucleotides
Limitations:
  Better fidelity on smaller fragments
  Sequencing sample preparation costly
  Expensive and large!
  Relatively low accuracy
  Low throughput
Application:
  Structural variations
  Whole transcript sequencing
  Small to medium sized genomes
  Methylation detection

## Slide 56
Technology Platforms - PacBio
PacBio RSII

## Slide 57
Technology Platforms - PacBio
Streptomyces sp. run data

## Slide 58
PacBio Sequel
  PacBio Sequel
    Read lengths up to >20kb
    6 hour run time
    1 million ZMWs
    ~7 Gb output
    Single molecule resolution
      SMRT = single molecule real-time
    Direct methylation detection

## Slide 59
Oxford Nanopore

## Slide 60
Oxford Nanopore
MinION
Notes: Minion Access Programme
Beta testing – open to all to apply
Registration fee of $1000

## Slide 61
Intro to nanopore sensing

## Slide 62
Example Nanopore runs
Data from DH?
Lambda phage (R6)
HMP mock community (R7)
Notes: MinIon Analysis Reference Consortium (MARC) 20 labs evaluating MinIon performance using E.coli
Air-Seq project
Drone flying across agricultural fields before and after crop spraying
Ebola - Africa Nick Loman and team from Birmingham
AGBT Nick Loman and Matt Loose sequencing at a conference!

## Slide 63
MinIon
Advantages
  Portable
  Cheap (?)
  Data analysis ‘on the fly’
Limitations
  Unavailable to the public
  Error rate is relatively high
  Dependent on input DNA length
Applications:
  Monitoring/surveillance
  Small genomes
  Accuracy not required
Notes: Ebola - Africa Nick Loman and team from Birmingham
MinIon – 1-2Gb per run 40-50Kb in length
512 Pores
PromethION 20-30Gb per run
1D and 2D reads – Latest chemistry has increased 2D reads – improved basecalling
HMW-DNA - development of extraction techniques

## Slide 64
Optical Mapping

## Slide 65
Optical Mapping
Opgen ARGUS
  For microbes
  Images ~1Gb/hr
  12Gb/card
  Fragments in 100s of Kb
BioNano Genomics Irys
  Microbes and beyond
  Images several Gb/hr
  100Gb/chip
  Megabase sized fragments

## Slide 66
OpGen Argus

## Slide 67
Comparative Genomics
Strain Typing
Whole Genome Sequence Assembly
Whole Genome Mapping

## Slide 68
acagctctcgagaggatcctcgtcgggatccctcgcgctcgagatcgcgtagcgctagagcgctctagaggctcgcggagagctcgcgcgagtgcgtcggggacacattcgaggatccagttagagatcggctcgtgctagaggcctgctcgtagagacacagatagacagatagagcggctcgctctcgctgctcggaagtcgctcgcgtaagttcgcgctggatcccacagctcgcgctgacacagtcgcgtagagatgcggctgagcgctggcgctgaggctggacagtgctgctgagctcggacagctcgtgtggcgcggatccgtgctcggcggatcctagggcgtgtcgcgtgctggatgcgctggtgggccccagtttggcggcgctcgcggctcggctgctggtcgcctgcttt
These patterns are specific to individual organisms and provide the ability to identify and compare isolates
Locates and measures distance between restriction sites in organism’s genome
Whole Genome Mapping

## Slide 69: OpGen Technology
DNA extraction
DNA stretched and immobilized
Scan fluorescent images, convert to digital data
Enzyme digest and
fluorescent stain to single DNA molecules
Digital data converted to single-molecule map set
Cells gently lysed to extract long genomic DNA molecules
DNA captured on charged glass slides in parallel channels of single DNA molecules
Whole Genome Mapping

## Slide 70
Image Analysis and Markup

## Slide 71
Overlapping single molecule maps are aligned to produce a map assembly covering an entire chromosome consensus map
Assembly into a Whole Genome Map
Notes: Each single molecule restriction map votes for or against there being a restriction cut site at a loci. While the final consensus map may look relatively simple, it was built upon these thousands of restriction maps.
certain amount of depth or coverage at any given location.
The quality controls in the software require at least 30X at any given site.

## Slide 72
Platform Overview
BioNano Irys
IRYS System

## Slide 73
Platform Overview
BioNano Irys

## Slide 74
Platform Overview
Optical Mapping
Advantages
  High level assessment
  of genome structure
Limitations
  Not technically generating
  sequence data
Applications
  Structural variation
  Comparative genomics
    Strain typing
  Refining references
    Gap sizing
    Identifying misassemblies

## Slide 75
Platform Overview
10X Genomics
Notes: Haplotyping and Single Cell

## Slide 76
Platform Overview
The GemCode technology has been adopted for use in multiple applications, including whole-genome phasing and structural variant analysis, de novo genome assembly, remapping of difficult regions of the genome, and dynamic gene expression of single cells.
GemCode Technology creates a unique reagent delivery system that partitions cells or
arbitrarily long DNA molecules (including >100 kb) and prepares sequencing libraries
in parallel such that all fragments produced within a partition share a common barcode.

## Slide 77
Platform Overview
10X Genomics
Each gel bead is functionalized with 10s of millions of copies of barcoded oligonucleotides. Every high quality oligo contains a defined 14 bp sequence representing one of 750,000 molecular barcodes plus components compatible with Illumina sequencing.
High throughput droplet-based reagent delivery using a microfluidic chip.
Gel bead-containing emulsions (GEMs) are created such that >90% of reactions contain a single molecular barcode.
Creattion of >100,000 GEMs per channel in a 5 minute instrument run time.

## Slide 78
Platform Overview
Applications
Resolve compound heterozygosity
(G->A substitution and 57kb deletion)
Detect Structural Variants - gene fusions,
duplications, deletions and translocations
(13Mb inversion)

## Slide 79
Platform Overview
Full spectrum of variants
SNVs, indels and large-scale structural
re-arrangements
Multi-megabase diploid de novo assembly
Preservation of phasing information for small
variants, structural rearrangements and novel sequence without the need of a reference
sequence.

## Slide 80
Fluidigm C1

## Slide 81
Platform Overview
Prime
Capture
Stain
Lyse
Amplify
Harvest

## Slide 82
Platform Overview
Advantages
  Single cell precision (96-cells)
  Easy to use
  Fast
Limitations
  IFC size of cell dependent (5-25 µm)
  Cell culture
  Recent issues with medium IFC
Applications
  Gene Expression
  Single cell genomics

## Slide 83
Platform Overview
 | METHOD | READ LENGTH | NUMBER OF READS | THROUGHPUT | RUN TIME
ILLUMINA HiSeq 4000 High Output | Sequencing by synthesis | Up to 150bp PE | 2.5 billion per flowcell | 750 Gb | 3.5 days
ILLUMINA HiSeq 2500 High Output v4 | Sequencing by synthesis | Up to 125bp PE | 2 billion per flowcell | 500 Gb | 6 days
ILLUMINA HiSeq 2500 Rapid | Sequencing by synthesis | Up to 250bp P.E | 300 million per flowcell | 150 Gb | 60 hours
ILLUMINA MiSeq | Sequencing by synthesis | Up to 300bp P.E | 25 million per flowcell | 13-15 Gb | 55 hours
PACBIO RSII | Real time sequencing | Average up to 20kb | 50 000 per SMRT cell | >1 Gb | 6 hours
Ion Proton | Semi-conductor sequencing | Up to 200bp | 60-80 million | Up to 10 Gb | 2-4 hours
OpGen Argus | Optical Mapping | 150kb -> 2Mb | ~2 000 per Map Card | 3Gb | 2 hours
BioNano Irys | Optical Mapping | > 1 Gb | Several Gb / hour | 100 Gb | 30 hours
Platform Overview

## Slide 84
Notes: 1) Antarctic diatom 2) Influenza 3) Moss (Physcomitrella patens) 4) White campion 5) Red clover 6) Tomato 7) Pea 8) Listeria 9) 10) Chloroplasts 11) Broad bean 12) Rapeseed 13) Barley 14) Willow15) Barrel clover 16) Tongue metagenome 17) FIV 18) Arabidopsis 19) Oats 20) Fungus21) Fission yeast 22) Mouse 23) Naked Mole Rat 24) Wheat 25) Perennial grass 26) Glomus intraradices 27) Immortal jellyfish 28) Cow 29) Kentish Plover 30) Common cuttelfish 31) Liver fluke 32) Green peach aphid 33) Late instar larvae 34) Dog 35) Turkey 36) Chicken 37) Amphioxus 38) Drosophila 39) Passionflower butterfly 40) Carp 41) White fly